## Slide 1: Battery Door Design Challenge
Megan Ying

## Slide 2: Problem Statement and Assumptions
Problem Statement
Users want to be able to replace batteries on the iPod
Assumptions
5th generation iPod Classic
  Dimensions: 103.5 mm x 61.8 mm x 10.5 mm
  Weight: 140 g
Other internal electronics do not exist
Users will accept a thicker product
Mechanism is cycled less than 1000x
  Duracell AA batteries last ~100 hours in constant use
  iPod Classic lasts ~5 years
Product will be mass manufactured
Door will pop open when released

## Slide 3: Requirements and Constraints
Functionality
User
Can sustain cycling over product lifespan
Withstands drop testing without failure
Withstands extreme temperature conditions without failure
Does not require excessive user force
Can be actuated using one hand
Is not prone to accidental actuation
Offers auditory or tactile feedback
Design
Minimizes number of components
Minimizes production time
Minimizes production costs
Minimizes weight addition
Minimizes thickness addition
Sleek and aesthetically pleasing

## Slide 4
Assumptions
5th generation iPod Classic
  Dimensions: 103.5 x 61.8 x 10.5 mm
  Mass: 140 g
Other internal components are out-of-scope
Users will accept a thicker product
  AA battery diameter: 14 mm
Product is cycled < 1000 times over lifespan
  Duracell AA batteries last ~100 hours during constant use
  iPod Classic lasts ~5 years
Product will be mass manufactured ( >100,000 units per year)
Door will pop open when released due to spring-loaded hinge
Requirements
Button requires minimal user effort to actuate, but resists accidental actuation
  Button press force of 2-5 N and travel distance of 1-3 mm
Door require minimal user effort to close, but resists accidental opening
  Closing force of < 8 N and opening force of > 20 N
Does not obstruct battery removal or handling
Prevents rattling or unwanted noise during use
Endures repeated use over product’s lifespan
Remains functional and secure during drops
Remains functional under extreme temperatures
Minimizes production costs and assembly time
Minimizes additional weight and space footprint
Maintains sleek and aesthetically pleasing appearance
Assumptions and Requirements

## Slide 5
Battery covers and water bottles with snap fits
1. Latch hooks onto door in locked position
2. Button is pressed and latch moves to release door
Inspiration
Concept
Moving Snap Fit Mechanism

## Slide 6
4. Button is pressed and hook travels to unlocked position
Push to open cabinets with touch latches
1. Button is pressed and hook travels down groove
3. Button is pressed and hook travels down groove
2. Button is released and hook sits in locked position
Inspiration
Concept
Push Release Mechanism

## Slide 7
Retractable pens with rotating cam body
1. Hook sits in groove of rotating part when locked
3. Button is released and hook travels up path
2. Button is pressed and hook travels down path
4. Hook is removed and part rotates to initial position
Inspiration
Concept
Rotating Body Mechanism

## Slide 8
Knobs with strike plate and sliding latch
1. Button is pressed and latches slide over fixed part
3. Button is pressed and latches slide over sliding part
2. Button is released and latches lock in place
4. Button is released and latches to unlocked position
Inspiration
Concept
Sliding Latch Mechanism

## Slide 9: Mechanisms: Flippable Snap Fit
Switches with spring toggle mechanism
1. Hinged latch is sitting in locked position
2. Button is pressed and hinged latch flips to unlocked position
Inspiration
Concept

## Slide 10: Comparing Mechanisms
Moving Snap Fit | Push Release | Rotating Body | Sliding Latch | Flippable Snap Fit
+ Less sensitive to tolerances + Not easily actuated + Simple components + Less components | + Button exists on door + Not easily actuated + Less components + Compact | + Button exists on door + Not easily actuated + Less components | + Button exists on door + Less sensitive to bending | + Less sensitive to tolerances + Simple components
- Sensitive to bending and wear - Button exists on housing | - Groove may jam - Sensitive to bending in multiple directions - Sensitive to tolerances - Complex components | - Groove may jam - Sensitive to tolerances - Downward hook force may not trigger rotation - Requires more space - Complex components | - Sensitive to tolerances - User may push down too far during locking - More components - Requires more space - Complex components | - Sensitive to bending and wear - May not actuate if button travel is small - Button exists on housing - More components

## Slide 11
Moving Snap Fit | Push Release | Rotating Body | Sliding Latch
+ Less sensitive to tolerances + Not easily actuated + Simple components + Less components | + Button exists on door + Not easily actuated + Less components + Compact | + Button exists on door + Not easily actuated + Less components | + Button exists on door + Less sensitive to bending
- Sensitive to bending and wear - Button exists on housing (user must put finger through door) | - Groove may jam - Sensitive to bending in multiple directions - Sensitive to tolerances - Complex components | - Groove may jam - Sensitive to tolerances - Downward hook force may not trigger rotation - Requires more space - Complex components | - Sensitive to tolerances - User may push down too far during locking - More components - Requires more space - Complex components
Comparing Mechanisms

## Slide 12
1. User presses down on the button, which is constrained by the chassis and pushed upward by the springs.
2. Button moves down and pegs apply a force to the latch slot, causing the latch to slide away from the door.
3. Downward force applied by latch to door is removed and spring loaded hinges cause door to pop open.
4. After replacing batteries, user applies a downward force to the door, engaging the snap fit mechanism.
Sliding Snap Fit Design

## Slide 13
Component | Quantity | Material | Manufacturing | Mass (g) | Cost per Unit ($) | Total Cost ($)
Top Chassis | 1 | ABS | Injection Molding | 6.9 | $0.35 | $0.35
Button | 1 | Aluminum 6061-T6 | Die Casting | 3.6 | $0.10 | $0.10
Latch | 1 | ABS | Injection Molding | 4.6 | $0.25 | $0.25
Springs | 2 | (Purchased) | (Purchased) | (Purchased) | $0.10 | $0.20
Screws | 4 | (Purchased) | (Purchased) | (Purchased) | $0.10 | $0.40
Bottom Chassis | 1 | ABS | Injection Molding | 8.6 | $0.45 | $0.45
Spring Loaded Hinge | 2 | (Purchased) | (Purchased) | (Purchased) | $0.10 | $0.20
Door | 1 | ABS | Injection Molding | 24.4 | $1.20 | $1.20
Door Cover | 1 | Aluminum 6061-T6 | Stamping | 4.7 | $0.15 | $0.15
 |  |  |  |  | Total | $3.30
* Remaining components assumed out-of-scope
Sliding Snap Fit Bill of Materials

## Slide 14
1. User presses down on the button, which is constrained by the top chassis and pushed upward by the springs.
2. Button moves down and applies a force to the tail of the latch, causing it to rotate about the peg.
3. Downward force applied by latch to door is removed and spring loaded hinges cause door to pop open.
4. After replacing batteries, user applies a downward force to the door, engaging the snap fit mechanism.
Rotating Snap Fit Design

## Slide 15
Component | Quantity | Material | Manufacturing | Mass (g) | Cost per Unit ($) | Total Cost ($)
Top Chassis | 1 | ABS | Injection Molding | 8.5 | $0.45 | $0.45
Button | 1 | Aluminum 6061-T6 | Die Casting | 3.8 | $0.10 | $0.10
Latch | 1 | ABS | Injection Molding | 2.4 | $0.15 | $0.15
Springs | 2 | (Purchased) | (Purchased) | (Purchased) | $0.10 | $0.20
Screws | 4 | (Purchased) | (Purchased) | (Purchased) | $0.10 | $0.40
Bottom Chassis | 1 | ABS | Injection Molding | 7.3 | $0.35 | $0.35
Spring Loaded Hinge | 2 | (Purchased) | (Purchased) | (Purchased) | $0.10 | $0.20
Door | 1 | ABS | Injection Molding | $1.20 | $1.20 | $1.20
Door Cover | 1 | Aluminum 6061-T6 | Stamping | $0.15 | $0.15 | $0.15
 |  |  |  |  | Total | $3.20
* Remaining components assumed out-of-scope
Rotating Snap Fit Bill of Materials

## Slide 16
 |  | Design 1: Sliding Snap Fit |  | Design 2: Rotating Snap fit | 
Criterion | Weight | Rating | Weighted Score | Rating | Weighted Score
Effectiveness | 5 | 4 | 20 | 3 | 15
User Experience | 4 | 4 | 16 | 3 | 12
Manufacturability | 4 | 3 | 12 | 3 | 12
Ease of Assembly | 4 | 3 | 12 | 3 | 12
Compactness | 4 | 3 | 12 | 4 | 16
Cost | 3 | 3 | 9 | 4 | 12
Total Score |  |  | 81 |  | 79
Decision Matrix

## Slide 17
6
7
8
Top Chassis
Button
Latch
Springs
Screws
Bottom Chassis
Door Cover
Door
Spring
Loaded Hinge
AA Battery
Battery Holder
Procedure
Bottom chassis is fixed to housing via screws
Button is assembled into latch so that button pegs will slide along latch slots
Springs placed onto bottom chassis posts
Latch and button assembly positioned over bottom chassis posts
Top chassis secured to bottom chassis via snap fit features
Battery holder fixed to housing (assumed out-of-scope)
Door cover secured to door via adhesive
Hinges assembled to door and housing via adhesive or screws
Sliding Snap Fit Components and Assembly

## Slide 18: Initial Button and Latch Calculations
Force for button to slide latch: 0.0033 N
μ = 0.2
Negligible friction between peg and slot
Negligible friction between latch and door
Rigid bodies: button peg moves with peg, snap fit moves with latch
FEA
Assumptions
Hand Calculations
Required spring constant: 0.01-0.875 N/mm
Max peg bending stress < fatigue strength
of SUS316 for 1000 cycles (300 MPa)
Button travel: 1.39 mm

## Slide 19: Door and Latch Calculations
FEA
Assumptions
Hand Calculations
Snap fit has constant cross-section
Deflection magnification factor Q = 1
Latch does not move during door closing (assume worst case)
Max door strain < allowable strain for ABS (7%)
Max door stress < fatigue strength of ABS for 1000 cycles (35 MPa)
Required force to close door: 6.1 N
μ = 0.2
Total deformation
Equivalent stress
Max deflection of door: 0.78 mm
Max equivalent stress: 49 MPa
Max force required: 28 N
Simulation assumes latch is a rigid body, latch does not move during door closing, and base of snap fit feature is fixed → use hand calculations

## Slide 20: Initial Door and Latch Calculations
Hand Calculations
Max strain < allowable strain for ABS (7%)
Max door stress < fatigue strength of ABS for 1000 cycles (35 MPa)
Required force to close door: 6.1 N
+
1
4, 5
6, 7
8
9
2, 3
No. | Description | Nom. | + Tol. | - Tol.
1 - 2 | Latch tip to latch slot center | 9.70 | 0.05 | 0.05
2 - 3 | Latch slot center to button peg center | 0.00 | 0.10 | 0.00
3 - 4 | Button peg center to button hole | -1.50 | 0.05 | 0.05
4 - 5 | Button hole to chassis post | 0.00 | 0.10 | 0.10
5 - 6 | Chassis post to screw hole center | 0.64 | 0.05 | 0.05
4 - 5 | Chassis screw hole center to housing | 0.00 | 0.10 | 0.10
 | housing screw hole center |  |  | 
5 - 6 | Housing screw hole center to edge | -11.00 | 0.10 | 0.10
6 - 7 | Housing edge to door tip | 2.95 | 0.20 | 0.20
Tolerance Analysis
Nominal overlap: 0.79 mm
RSS Max overlap: 1.09 mm
RSS Min overlap: 0.51 mm